## Slide 1
Template #: DCON-029-1010 R8
Sean Sinclair, Environment Superintendent
Processed Kimberlite to Mine
Workings - Scoping Meeting
Introduction and Project Overview

## Slide 2: Presentation Outline
Introduction and Project Overview
Water Quality Modelling Approach
Scope of the Environmental Assessment

## Slide 3: Diavik Team
Sean Sinclair – Environment Superintendent
Gord Macdonald – Closure Manager
Kofi Boa-Antwi – Regulatory Advisor
Mark Nelson – Environment Advisor

## Slide 4: Rio Tinto in Canada
Supporting a team of 15 000
35 sites across the country
Producing the materials essential for human progress
Montreal recently named one of the company’s three global hubs
Rio Tinto Operations in Canada
Aluminum
Energy & Minerals
Copper & Diamonds
Rio Tinto Corporate Support Offices
4

## Slide 5: The Diavik diamond mine
Rio Tinto Operations in Canada
5

## Slide 6: Diavik at a glance
  Located at Lac de Gras approximately 300 km northeast of Yellowknife
  Joint Venture: 60% Rio Tinto (owner and operator) and 40% Dominion Diamond Mines (acquired by The Washington Companies)
  ~1,100 employees including contractors
  5 local Indigenous groups
  Discovered in 1995, operations commenced in 2003
  Produces around 6-7 million carats per annum
  Over 100 million carats produced since 2003
  The current mine plan has production ending in 2025
6

## Slide 7: Bringing the two billion year old gems to the surface
Four kimberlite pipes mined using open pit and underground mining methods
        A154 North
        A154 South
        A418
        A21
Above ground processing plant has a ~2.4 million tonne capacity
In Yellowknife, we clean and sort Diavik rough diamonds for their onward sales and marketing journey

## Slide 8: Regulatory Approvals / Authorizations for the Diavik Diamond Mine Project
Approvals/Authorizations for Diavik to date not limited to the following:
Canadian Environmental Assessment Act Approval
Environmental Agreement
Surface Leases
Fisheries Act Authorizations
Navigation Protection Act Approvals
Water Licence

## Slide 9: Purpose of the Proposal / Application
To request an amendment to the Water Licence to permit the option of deposition of Processed Kimberlite (PK) material into Mine Workings (A418, A154, and A21 pits)
“Mine Workings” means the underground and/or open pit area resulting from the development of an ore body
Mackenzie Valley Environmental Impact Review Board is conducting an environmental assessment (EA) on the Proposal

## Slide 10: PK Production and Storage
Based on the current mine plan, the PKC will be full in 2021 without additional dam raise beyond current approvals
Underground mining of the A154S and A418 kimberlite pipes will be completed by 2022
Underground mining of the A154N kimberlite pipe will be completed in 2025
Open pit mining of the A21 kimberlite pipe will be completed by 2023
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
A154N | 748087.7 | 834716.5147 | 923930.2673 | 962652.1696 | 1059461.8286 | 1115553.5282 | 1222630.3791 | 1187868.0421 | 168194.9162
A154S | 498001.6356 | 387634.8756 | 302792.9348 | 276863.8652 | 123423.4318 | 0 | 0 | 0 | 0
A418 | 1074401.2136 | 1077810.4492 | 884877.8217 | 809595.3152 | 211004.829 | 0 | 0 | 0 | 0
A21 | 0 | 205000 | 499000 | 595000 | 1096000 | 625000 | 0 | 0 | 0

## Slide 11: Current PK Storage
Processed kimberlite is currently stored within the Processed Kimberlite Containment (PKC) Facility
The PKC Facility is surrounded by a lined dam that DDMI has constructed and made higher over the years
The amount of storage area left within the PKC will not fit the amount of processed kimberlite that will be produced during the remaining years of mining
PKC dam expansion opportunities are limited by the size of East Island

## Slide 12: Conceptual Drawings for A418
Deposition strategy to be finalized and included in Processed Kimberlite Containment in Mine Workings Design Report

## Slide 13: Benefits of the Deposition of PK to Mine Workings
Improves health and safety related to operations and closure
Reduces environmental risks related to PK storage
Ensures certainty in PK storage capacity for the life-of-mine
Enhances operational flexibility
Reduces capital expenditures for the life-of-mine
Reduces closure risks

## Slide 14: Assessment of Potential Environmental Risks and Impacts
Assessed the potential for adverse impacts to biotic and abiotic components, including water quality and fish and fish habitat
Assessment based on robust data from site specific studies, literature review, and Traditional Knowledge
Assessed operational, health and safety, and environmental risks, including the potential for accidents and malfunctions

## Slide 15: Assessment of Potential Environmental Risks and Impacts
Applied credible assumptions where scientific uncertainty exists
Applied conservatism and the precautionary approach
Certainty and confidence in results informed by ongoing operations and on modelling
Monitoring programs and adaptive management

## Slide 16: Assessment of Potential Environmental Risks and Impacts
Committed to protecting the health and safety of workers and the environment in executing the proposal
Committed to ensuring PK to Mine Workings does not result in significant adverse impacts to the environment

## Slide 17: Stakeholder Engagement
Proposed PK to Mine Workings informed by DDMI’s ongoing engagement with stakeholders
PK to Mine Workings addresses concerns regarding the long-term stability and environmental risks of the Processed Kimberlite Facility
Engaged stakeholders on potential impacts, proposed mitigation measures, the acceptability of residual impacts, and how mitigation might be enhanced

## Slide 18: Stakeholder Support
Broad support for the Proposal among our Participation Agreement partners and communities
PK to Mine Workings not likely to be a cause of significant public concern

## Slide 19: Alternatives Assessment / Options Analysis
Four (4) options considered as part of preliminary studies:
        Life of Mine (LOM) PK storage through traditional dam raise.
        LOM PK storage through current PKC dam height and deposition to mine workings.
        LOM PK storage through current PLC dam height and alternative onsite storage options.
        Combination of PKC dam raise and deposition to mine workings (Preferred Option).
Option | Key Advantages | Key Disadvantages
1. Traditional Dam Raise | permitted known approach | high cost footprint restrictions new construction necessary limited closure options
2. A418 Deposition with Current Dam Height | lower cost maximum use of existing storage capacity no new dam construction enhanced closure options | license amendment high risk of running out of PKC storage before A418 is available.
3. Additional On-Site Storage | no new dam construction lowest cost enhanced use of existing facilities | loss of original facility functionality license amendment site runoff risk expanded closure footprint
4. PKC Dam Raise and A418 Deposition | limits risk of running out of storage space maximize use of existing storage capacity enhanced closure options | moderate cost new dam construction necessary license amendment

## Slide 20
Template #: DCON-029-1010 R8
Gord Macdonald, Closure Manager
Processed Kimberlite to Mine
Workings - Scoping Meeting
Water Quality Modelling Approach

## Slide 21: Water Quality Modelling Approach CE-QUAL-W2: a two dimensional, laterally averaged, hydrodynamic, and water quality model

## Slide 22: Processed Kimberlite Deposition into Mine Workings
Conceptual model – consolidation & pore water release over time
As conceptualized
As modelled

## Slide 23
Parameters | Unit | AEMP Benchmark | Lac de Gras2 | Scenario 2-a | Scenario 3-a | Scenario 4-a
 |  |  |  | at Depth of 40 m Below Surface | at Depth of 40 m Below Surface | at Depth of 40 m Below Surface
Chloride | mg/L | 120 | 1.9 - 5.2 | 3.5 | 3.7 | 3.5
Sulfate | mg/L | 100 | 2.19 - 5.47 | 4.0 | 4.7 | 4.0
Nitrate as nitrogen | mg/L | 3 | 0.001 - 0.105 | 0.063 | 0.12 | 0.064
Aluminum | μg/L | 87 | 4.46 - 9.74 | 6.3 | 6.3 | 6.3
Arsenic | μg/L | 5 | 0.202 - 0.401 | 0.28 | 0.3 | 0.28
Cadmium | μg/L | 0.1 | 0.0025 - 0.0054 | 0.0029 | 0.0042 | 0.0029
Copper | μg/L | 2 | 0.5 - 0.661 | 0.59 | 0.6 | 0.59
Lead | μg/L | 1 | 0.0025 - 0.007 | 0.0035 | 0.0048 | 0.0035
Molybdenum | μg/L | 73 | 0.265 - 2.79 | 0.99 | 2.1 | 1.0
Nickel | μg/L | 25 | 0.642 - 0.886 | 0.77 | 0.79 | 0.77
Uranium | μg/L | 15 | 0.092 - 0.157 | 0.12 | 0.12 | 0.12
Zinc | μg/L | 30 | 0.11 - 0.38 | 0.21 | 0.48 | 0.21
Pit Lake Modelling Results1
Surface water quality remains below Benchmarks and similar to Lac de Gras
Results for A418 taken from response to Technical Session IR-5
Range of measured concentrations at AEMP MF3-1 and MF3-2 (DDMI 2017)
2a – 5.0 Mm3 deposited PK
3a – 5.0 Mm3 deposited PK plus 5.0 Mm3 of dredged PK slimes
4a – Scenario 2a but with initial decant water level at 15m vs 5m

## Slide 24
Template #: DCON-029-1010 R8
Kofi Boa-Antwi, Regulatory Advisor
Processed Kimberlite to Mine
Workings - Scoping Meeting
Scope of the EA

## Slide 25: Scope of the Environmental Assessment
EA to focus on the Closure Phase
EA scope to be for storage of PK in mine workings
An unanticipated mixing event to be considered within “Accidents and Malfunctions”
Effects Criteria and Significance to be as defined in the Comprehensive Study Report (1999) for the Diavik Diamond Mine Project

## Slide 26: Scope of the Environmental Assessment, cont’d
Wildlife effects assessment to be limited to Caribou
“Cultural use of the area post-closure” relates to fishing and/or drinking of water within pit lakes and Lac de Gras
No requirement to develop additional baseline data – will reference existing data used in previous assessments
Cumulative impacts will only be considered where there are residual impacts

## Slide 27: Questions?